## Slide 1: Main Algorithm: Step 1: START Step 2: Display Main Menu 1. Beam Design Calculator 2. Column Design Calculator 3. Slab Design Calculator 4. Footing Design Calculator 5. Truss Analysis 6. Material Properties Calculator 7. Load Calculator 8. Deflection Calculator 9. Shear Force and Bending Moment 10. Steel Design Calculator 11. Save/Load Design 12. Exit

## Slide 2
Step 3: INPUT user choice Module 1: Beam Design Calculator Step 4: IF choice = 1 (Beam Design Calculator) Step 4.1: Display Beam Design Sub-Menu: a. Simply Supported Beam b. Cantilever Beam c. Fixed Beam d. Continuous Beam Step 4.2: INPUT beam type selection Step 4.3: INPUT beam parameters: Length (L) Width (b) Depth (d)

## Slide 3
8. Concrete grade (fck)
Steel grade (fy)
Loading type (UDL/Point Load)
Load magnitude
Step 4.4: CALCULATE:
Effective depth: d_eff=d-clear cover-dia/2
Maximum bending moment: M_max
Maximum shear force: V_max
Required area of steel: Ast = (M/(0.87xfyxjxd))
Number of bars required
Spacing of stirrups

## Slide 4
Step 4.4: CALCULATE:
Effective depth: d_eff=d-clear cover-dia/2
Maximum bending moment: M_max
Maximum shear force: V_max
Required area of steel: Ast = (M/(0.87xfyxjxd))
Number of bars required
Spacing of stirrups
Check for deflection
Check for shear
Step 4.5: Display design results with diagram
Step 4.6: GOTO Step 2
Module 2: Column Design Calculator
Step 5: ELSE IF choice = 2 (Column Design Calculator)
Step 5.1: INPUT column type:
a. Rectangular Column

## Slide 5: b. Circular Column c. L-shaped Column d. T-shaped Column Step 5.2: INPUT column parameters: Height (H) Cross-sectional dimensions Axial load (P) Moment (M) if any Concrete grade (fck) Steel grade (fy) Effective length factor Step 5.3: CALCULATE: Slenderness ratio: A = (1_eff/r) Check if short or slender column Minimum eccentricity

## Slide 6
Required steel area: Asc Lateral ties spacing Load carrying capacity Step 5.4: Display design details with reinforcement layout Step 5.5: GOTO Step 2 Module 3: Slab Design Calculator Step 6: ELSE IF choice = 3 (Slab Design Calculator) Step 6.1: INPUT slab type: a. One-way Slab b. Two-way Slab c. Flat Slab Step 6.2: INPUT slab parameters: Length (Lx) Width (Ly) Thickness (D) Support conditions

## Slide 7
Step 6.2: INPUT slab parameters:
Length (LX)
Width (Ly)
Thickness (D)
Support conditions
Live load (LL)
Dead load (DL)
Concrete grade (fck)
Steel grade (fy)
Step 6.3: CALCULATE:
Effective span
Total load: w = DL+LL

## Slide 8
IF one-way slab: ly/lx > 2
IF two-way slab: ly/lx < 2
Bending moments (Mx, My)
Required steel area in both directions
Spacing of reinforcement
Check for deflection
Check for shear
Step 6.4: Display design with reinforcement details
Step 6.5: GOTO
Step 2

## Slide 9
Module 4: Footing Design Calculator
Step 7: ELSE IF choice = 4 (Footing Design Calculator)
Step 7.1: INPUT footing type:
a. Isolated Footing
b. Combined Footing
c. Strap Footing
d. Mat Foundation
Step 7.2: INPUT parameters:
Column load (P)
Safe bearing capacity of soil (SBC)
Column dimensions
Concrete grade (fck)

## Slide 10
Steel grade (fy)
Step 7.3: CALCULATE:
Required footing area: A =P/SBC
Footing dimensions (LxB)
Footing depth based on punching shear
Bending moment at critical section
Steel reinforcement required
Check for one-way shear
Check for two-way shear (punching)
Development length
Step 7.4: Display footing design with details
Step 7.5: GOTO Step 2

## Slide 11
Module 5: Truss Analysis
Step 8: ELSE IF choice = 5 (Truss Analysis)
Step 8.1: INPUT truss type:
a. Simple Truss
b. Roof Truss
c. Bridge Truss
Step 8.2: INPUT truss parameters:
Number of joints (n)
Number of members (m)
Support conditions
FOR each joint: INPUT coordinates (x, y)

## Slide 12
FOR each member: INPUT connectivity (joint i to joint j)
INPUT external loads at joints
Step 8.3: CALCULATE:
Check stability: m+r=2n (where r = reactions)
Apply Method of Joints OR Method of Sections
FOR each joint:
Apply equilibrium equations: EFX = 0, 2F = 0
SOLVE for member forces
Determine tension/compression in each member

## Slide 13
Calculate reactions at supports
Step 8.4: Display member forces with diagram
Step 8.5: Highlight critical members
Step 8.6: GOTO Step 2
Module 6: Material Properties Calculator
Step 9: ELSE IF choice = 6 (Material Properties Calculator)
Step 9.1: Display Material Properties Menu:
a. Concrete Properties
b. Steel Properties

## Slide 14
c. Timber Properties
d. Composite Materials
Step 9.2: INPUT material selection
Step 9.3: IF Concrete selected:
INPUT concrete grade (M20, M25, M30, etc.)
Display:
Characteristic strength (fck)
Modulus of elasticity: Ee = 5000/fck

## Slide 15
Density
Poisson's ratio
Permissible stresses
Step 9.4: IF Steel selected:
INPUT steel grade (Fe415, Fe500, etc.)
Display:
Yield strength (fy)
Ultimate strength (fu)
Modulus of elasticity: Es = 200000 N/mm²
Density
Permissible stresses

## Slide 16
Module 7: Load Calculator
Step 10: ELSE IF choice =7 (Load Calculator)
Step 10.1: Display Load Calculator Menu:
a. Dead Load Calculator
b. Live Load Calculator
c. Wind Load Calculator
d. Seismic Load Calculator
e. Snow Load Calculator
Step 10.2: INPUT load type selection
Step 10.3: IF Dead Load:
INPUT material type and dimensions

## Slide 17
RETRIEVE unit weight from database
CALCULATE: DL = Volume × Unit Weight
Step 10.4: IF Live Load:
INPUT occupancy type (residential, office, etc.)
RETRIEVE standard LL from IS code
CALCULATE total live load
Step 10.5: IF Wind Load:
INPUT:
Building height
Basic wind speed (Vb)
Terrain category

## Slide 18
Structure dimensions
CALCULATE:
Design wind speed: Vzk1xk2xk3x Vb
Wind pressure: pz = 0.6 × Vz
Wind force on structure
Step 10.6: IF Seismic Load:
INPUT:
Seismic zone
Soil type
Building weight

## Slide 19
Importance factor
Response reduction factor
CALCULATE:
Base shear: Vb = Ah x W
Distribution of forces to floors
Step 10.7: Display calculated loads
Step 10.8: GOTO Step 2
Module 8: Deflection Calculator
Step 11: ELSE IF choice = 8 (Deflection Calculator)
Step 11.1: INPUT beam/member type:
a. Simply Supported Beam
b. Cantilever Beam
c. Fixed Beam

## Slide 20
Step 11.2: INPUT parameters:
Length (L)
Moment of inertia (1)
Modulus of elasticity (E)
Loading (UDL/Point Load)
Load magnitude (w or P)
Step 11.3: CALCULATE deflection based on beam type:
Simply Supported with UDL: 8 = (5xwxL)/(384×EXI)
Simply Supported with Point Load: 8 = (PL)/(48xExI)

## Slide 21
Cantilever with UDL: 8 = (wxL)/(8×ExI)
Cantilever with Point Load: 8 (PxL)/(3xExI)
Step 11.4: CHECK if deflection is within permissible limits: L/250
Step 11.5: Display deflection value and status
Step 11.6: Plot deflection diagram
Step 11.7: GOTO Step 2
Module 9: Shear Force and Bending Moment
Step 12: ELSE IF choice = 9 (Shear Force and Bending Moment)
Step 12.1: INPUT beam type and support conditions

## Slide 22
Step 12.2: INPUT:
Beam length (L)
Number of loads
FOR each load: INPUT position and magnitude
Support locations
Step 12.3: CALCULATE reactions at supports:
Apply Fy = 0
Apply ΣΜ = 0
SOLVE for reactions
Step 12.4: CALCULATE Shear Force:

## Slide 23
Divide beam into segments
FOR each segment:
Calculate SF = Reaction - Loads up to that point
Step 12.5: CALCULATE Bending Moment:
FOR each segment:
Calculate BM EM about that point
Step 12.6: Find maximum values:
V_max (maximum shear force)
M_max (maximum bending moment)
Locations of maximum values
Step 12.7: Plot SF and BM diagrams
Step 12.8: Display point of contraflexure if any
Step 12.9: GOTO Step 2

## Slide 24
Module 10: Steel Design Calculator
Step 13: ELSE IF choice = 10 (Steel Design Calculator)
Step 13.1: Display Steel Design Menu:
a. Steel Beam Design
b. Steel Column Design
c. Connection Design
d. Plate Girder Design
Step 13.2: INPUT steel design type
Step 13.3: IF Steel Beam:

## Slide 25
INPUT:
Span (L)
Loading (UDL/Point)
Steel section type (I. C, Angle)
CALCULATE:
Maximum moment and shear
Required section modulus: Z=M/fb
SELECT appropriate section from steel tables
RETRIEVE all parameters

## Slide 26
Check for deflection
Check for shear
Check for web buckling
Check for lateral-torsional buckling
Step 13.4: IF Steel Column:
INPUT:
Height
Axial load
End conditions

## Slide 27
CALCULATE:
Effective length
Required area: A =P/fc
Slenderness ratio
SELECT section
Check buckling strength
Step 13.5: Display design results with section properties
Step 13.6: GOTO Step 2
Module 11: Save/Load Design

## Slide 28
Step 14: ELSE IF choice = 11 (Save/Load Design)
Step 14.1: Display sub-menu:
a. Save Current Design
b. Load Previous Design
c. View Saved Designs
d. Delete Design
Step 14.2: IF Save:
INPUT design name
SAVE all parameters and results to file/database
Display "Design Saved Successfully"
Step 14.3: IF Load:
Display list of saved designs
SELECT design to load
RETRIEVE all parameters

## Slide 29
Program Termination
Step 15: IF choice = 12
Display "Thank You for Using the Calculator"
EXIT system
Step 16: STOP
Key Formulas Used
Beam Design
Ast=M/(0.87xfyxjxd)

## Slide 30
Shear stress: TV = V/ (bxd)
Column Design
Slenderness ratio: λ = leff / r
Pu = 0.4 x fckx Ac + 0.67 x fyx Asc
Deflection
Simply Supported (UDL): 8 = (5wL+)/(384EI)
Cantilever (Point Load): 8 = (PL)/(3EI)
Wind Load
pz=0.6 x Vz
Vzk1xk2 × k3 x Vb
Seismic Load
Base Shear: Vb = Ah x W

## Slide 31
Ah = (2/2) x (I/R) × (Sa/g)
Notes
All calculations follow IS Code standards (IS 456, IS 800, IS 875, IS 1893)
Units should be consistent throughout calculations
Safety factors and load factors as per code requirements
Design should satisfy both strength and serviceability criteria