## Slide 1
C PROGRAM:
Multi‑Module Structural & Material Design Calculator
For educational / school use (basic concepts only)
--------------------------------------------------
Project structure (logical modules in one file for simplicity):
1. material.c / material.h -> material properties
2. loads.c / loads.h -> load calculations
3. beam.c / beam.h -> simple beam design checks
4. main.c -> menu & integration
*/
#include <stdio.h>
#include <math.h>
/* ================= MATERIAL MODULE ================= */
typedef struct {
char name[20];
double density; // kg/m^3
double youngsModulus; // Pa
double yieldStress; // Pa
} Material;

## Slide 2
Material createMaterial(const char *name, double density, double E, double fy) {
Material m;
snprintf(m.name, sizeof(m.name), "%s", name);
m.density = density;
m.youngsModulus = E;
m.yieldStress = fy;
return m;
}
void printMaterial(Material m) {
printf("Material: %s\n", m.name);
printf("Density: %.2f kg/m^3\n", m.density);
printf("Young's Modulus: %.2e Pa\n", m.youngsModulus);
printf("Yield Stress: %.2e Pa\n", m.yieldStress);
}
/* ================= LOAD MODULE ================= */
double uniformLoad(double loadPerMeter, double length) {
return loadPerMeter * length; // Total load (N)
}

## Slide 3
double pointLoadMoment(double load, double distance) {
return load * distance; // Moment (Nm)
}
/* ================= BEAM MODULE ================= */
typedef struct {
double width; // m
double height; // m
} RectangularSection;
double momentOfInertia(RectangularSection s) {
return (s.width * pow(s.height, 3)) / 12.0;
}
double bendingStress(double moment, RectangularSection s) {
double I = momentOfInertia(s);
double y = s.height / 2.0;
return (moment * y) / I;
}
int isBeamSafe(double stress, Material m) {
return stress <= m.yieldStress;
}

## Slide 4
/* ================= MAIN MODULE ================= */
int main() {
int choice;
Material steel = createMaterial("Steel", 7850, 2.0e11, 250e6);
RectangularSection beam;
printf("STRUCTURAL & MATERIAL DESIGN CALCULATOR\n");
printf("-----------------------------------\n");
printf("1. View Material Properties\n");
printf("2. Beam Bending Stress Check\n");
printf("Enter choice: ");
scanf("%d", &choice);
if (choice == 1) {
printMaterial(steel);
}
else if (choice == 2) {
double loadPerMeter, length;

## Slide 5
printf("Enter beam width (m): ");
scanf("%lf", &beam.width);
printf("Enter beam height (m): ");
scanf("%lf", &beam.height);
printf("Enter uniform load (N/m): ");
scanf("%lf", &loadPerMeter);
printf("Enter beam length (m): ");
scanf("%lf", &length);
double totalLoad = uniformLoad(loadPerMeter, length);
double maxMoment = (totalLoad * length) / 8.0; // Simply supported beam
double stress = bendingStress(maxMoment, beam);
printf("Max bending stress: %.2e Pa\n", stress);
if (isBeamSafe(stress, steel))
printf("Beam is SAFE under bending.\n");
else
printf("Beam is NOT SAFE under bending.\n");
}
else {
printf("Invalid choice.\n");
}
return 0;
}